## Slide 1: Power Spectral Density
.

## Slide 2: Properties of RXX (Γ)
If the process is at least w.s.s then the auto correlation exhibits the following properties
  .
  .

## Slide 3: Things that can be deduced from autocorrelation
Autocorrelation of a signal tells us how “related” are samples spaced at any particular lag τ
  (on average – expectation)
Rxx(τ) = 0 implies that samples spaced by τ are unrelated
  Uncorrelated
Rxx(τ) < 0 implies that samples spaced by τ tend to be opposite in sign
  Negatively correlated
x(k)
Rxx(τ)
Lag τ
k
Notes: The autocorrelation provides a means of describing the interdependence of two r.v. observed in a random process X(t) Γsecond apart. The more rapidly X(t) changes with time the more rapidly Rxx(Γ) will decrease from its maximum at Rxx(0).

## Slide 4: Autocorrelation Application Pitch Detection in Speech
“aah”
“shh”
Notes: Autocorrelation used in speech analysis for pitch detection – note the difference in the autocorrelation function between “ahh” and “shh” (quasi persiodic vs noise). For “ahh” autocorrelation peaks at 0, and at intervals of the pitch, for “shh” it peaks at 0, then rapidly decays away (sames vary uncorrelated).

## Slide 5: Fourier Transform
Notes: To date the focus for the Random Processes has been in the time domain – mean and autocorrelation provide information about the time domain characteristics.
For deterministic signals we look at them both in the time domain and frequency domain
We use the Fourier Transform to transform the time domain signals into the frequency domain – to look at the frequency content (X(f) is typically an amplitude spectrum).
It would make sense then to view Random Processess in the frequency domain ?

## Slide 6: What is the Fourier Transform of a Random Process ?
F {X(t)}=?
Notes: Since X(t) is is a random process
There is no guarantee that a fourier transform exists for each sample function
If each sample function does have a well-defined Fourier transform, we are still left with the problem that X(f) is a random process.
In our earlier lectures we described the temporal characterics of a random process in terms of deterministic functions of mean and autocorrelation. – so we seek a deterministic description of the spectral characteristics of a random process – and it turns out the power spectral density fits that role.

## Slide 7: The Power Spectral Density
The power spectral density, SXX(f) and autocorrelation function of a wide sense stationary (wss) random process X(t) form a Fourier transform pair,
Together they constitute the Wiener-Khintchine relations, and they show that if either the power spectral density or the autocorrelation of a random process is known then the other can be calculated exactly.
For practical purposes the power spectral density is the more useful parameter.
Notes: For a deterministic signal it is customary to take the Fourier Transform and then determine the amplitude spectral density, for random processes we determine the power spectral density with is based on the second moment – autocorrelation – so the spectral density can be thought of as the second moment of the random process in the frequency domain.

## Slide 8: Properties of the Power Spectral Density (psd)
The zero frequency power of the psd of a wss random process equals the area under the autocorrelation function:
The mean-square value of a wss random process equals the total area under the graph of the power spectral density:
The psd of a wss random process is always nonnegative
The power spectral density of a real-valued random process is an even function of frequency:
Notes: Let f=0
Let τ=0, note Rxx(0)= E[X(t)^2] – so the average power of X(t) is calculated as the area under the psd graph. Whilst the average power can be calculated from a single value of the autocorrelation function in the time, it is spread across all the frequencies in the frequency domain – which is why its called the power spectral density.
Because the autocorrelation function is semi-definite, it can be shown that the psd is nonnegative.
Substitute –f for f and then - τ for τ,

## Slide 21: Power spectrum - example
Have a sample function from a Random Process
Compute autocorrelation
Compute Fourier Transform
τ
k
x(k)
Rxx(τ)
Sxx(f)
f

## Slide 22: Power spectrum - computation
Computing RXX requires large number of calculations
If x[n] is stationary and ergodic, can divide x[n] into shorter segments and average across segments (ensemble average across segments)
k
x(n)
x(i)(k)
k
τ
FT

## Slide 23: Power spectrum – FFT method
Don’t actually need the autocorrelation – all we are after is the power spectrum.
  What we want is expected value of squared spectrum
So, divide signal into segments, take FFT of each segment, and average the squared magnitude
x(i)(k)
k
f
SXX(f)
f
|FFT|2
E{.}